## Slide 1: Energy-Efficient Robust Beamforming for LEO Satellite
Prakrit Parajuli

## Slide 2: Motivation
Real satellites have limited onboard power
Sum-rate maximization→always spends fill power budget.
The real question isn't "how much rate" but " how much rate per watt"
Solving this rate-per-watt problem optimally means re-solving a non-convex fractional program every channel updates, too costly for real-time onboard use.
RL instead learns a direct policy; channel errors→beamforming decisions: near-optimal efficiency, no per step optimization.

## Slide 3: System model
Single LEO satellite, Uniform Lineararray(ULA), N=16 antennas.
K=3 single antenna ground users
Satellite alditude d₀ = 600 km, carrier frequency f=2GHz, transmit power budget P = 100W
LoS channel model with CSIT error model as AoD error +large-scale fading
Variables needs to be in math mode -> italic

## Slide 5: Sum rate Maximization
These inbetween slides are not necessary for that kind of a presentation

## Slide 6: Baseline: Sum Rate Maximization
Our earlier work on this system maximizes the following objective:
Where the instantaneous sum rate over all K users is:
Subject to the total radiated power budget P.
The precode (MMSE, learned SAC precoder) rescales ist output to land exactly on this power budget.
Underthis rate-only objective, using more tranmsit power is never worse, so the optimum always saturates the full power budget.
Directly put SINR instead of Gamma
Write maximization problem as maximization problem, ie max_W R

## Slide 7: Energy Efficiency

## Slide 8: Our new objective: Energy Efficiency
We have consider the more realistic scenario by adding electrical power consumption model:
And formulate a new maximization problem – Energy efficiency:
Precoder now only rescale down when hte power is over budget, this lets the policy choose to use less than the full budget when that is more efficient.

## Slide 9: SAC in Practice

## Slide 10: How we solve it
Each simulation step, in a loop:
  channel estimate → Actor network → proposed precoding matrix W → reward → store & learn
Rate-over-power is ratio, akward for RL to maximize directly, classical Dinkelbach's transmormation gave us the motivation to turn it into the substraction, implement directly into the reward:

## Slide 11: Results

## Slide 12: Results
MMSE and SAC maximize for rate always sped full power budget; our energy-Efficient SAC do not and stays robust as CSIT error grows:

## Slide 13: Results: What this Looks like Spatially
Comparing where the regular (100 W) SAC and Energy Efficient SAC actually point their antenna beamd for the same users:

## Slide 14: Contact
Name
Telefon
Email
Name
Telefon
Email
Name
Telefon
Email
Name
Telefon
Email
Name
Telefon
Email
Name
Telefon
Email